## Slide 1: Deathray: A hardware test platform Preliminary Design Review
Vanderbilt University, March 15th 2012

## Slide 2: Group Members: Nadiah Zainol Abidin Anas Alfuntukh Jack Minardi Customer/Sponsor: Institute of Space and Defense Electronics (ISDE) Advisor: Prof. Daniel Loveless, Research/Develop Engineer

## Slide 3: Agenda
Overview (j)
Graphical User Interface Design (j and a)
Hardware Control (a and n)
Modularity (anas)
API (j)
Robustness (a)
Testing (n)
Challenges (n and j)

## Slide 4: Statement of Work
The goal of this project is to design a graphical user interface to control and visualize integrated circuits radiation experiments in real time
Why does it have to be in real time?
  Detect any kind of error at early stage
    Device under testing
    Equipment malfunction
What are the advantages of using this software?
  Save time
  Save $$$$

## Slide 5: Graphical User Interface Goals
Be able to set up new experiments
Be able to save experiment configurations
Be able to poll active hardware [DONE]
Be able to plot in real time while accessing data [~DONE]
Be able to load in configuration of previous experiments
Be able to access data from previous experiments [DONE]
Be able to integrate GPIB control with FPGA scripts
Fully implement power supply, digital multimeter, oscilloscope [~DONE]

## Slide 6: Draft of GUI design
Welcome Window
Experiments
Load Experiment
Saved configurations
New Experiment
Data
Configure settings
List of experiments
Data of experiment
(read only)
Edit/confirm
confirm
Run analysis window

## Slide 7: Current GUI progress

## Slide 8: Hardware Control
So how does the software communicate with the hardware?
Series of commands using the GPIB
Series of tools using the FPGA

## Slide 9: FPGA control
SE Test System (made of several components)
3.3 V
GND
FPGA
I/O
DUT
Computer
USB/serial

## Slide 10: GPIB Control
‘General Purpose Interface Bus’
The de facto standard of controlling hardware using a PC
A bus system for Test and Measurement applications
This networked system has all features that are required to create a measurement system.
Remote control of instruments, real-time response capability, data handshake for reliable operation are few of the features of the GPIB.

## Slide 11: Hardware
GPIB gateway
Digital multimeter
hp34401a
DC power supply
hpe3631a

## Slide 12: Hardware
Oscilloscope
dso6032a

## Slide 13: GPIB: SCPI commands
Standard Commands for Programmable Instruments
standard for syntax and commands to use in controlling programmable test and measurement devices
SCPI commands to an instrument may either perform a set operation (e.g. switching a power supply on) or a query operation (e.g. reading a voltage)

## Slide 14: Modularity
-What is modularity?
-Subdivide the modules by commands because one command can work with multiple device
-should be easy for user to write new commands for new device
-Easy for extending the software in the future

## Slide 15: API
class FileProcessor:
def init(self, filesList):
self.filesList = filesList
#Fill in the following
self.processedData = [{}]
self.displayData = []
self.tableData = []

## Slide 16: API
Have access to 4 plot windows
Uses PyQwt plotting library
  Easy to modify
View is based off of the tree list
Documentation and sample code

## Slide 17: Robustness
Software has to be robust from:
People who are not familiar with the program
People who wants to hack the program
People who might try to break the program on purpose
How?
Checking method
Documentation (user manual, developer manual)
Hide implementation details (such as GPIB)
Sanitizing inputs
Notes: Specified choices of the users

## Slide 18: Assumptions
User sets up physical GPIB devices
Will not be used for publication quality plots
User will process FPGA data (in python)
Access to FGPA output files

## Slide 19: Challenges
Device SCPI (data_acquisition)
- Return ‘15’ error: does not help us detect if ‘junk’ was written
Inconsistency in the user manual
  -Time Scale issue for oscilloscope: only goes from 2ns to 50s instead of 500ps to 50s
Testing
-unit testing
-user testing
Building software with dumb user expectation
Security
Dealing with failing hardware

## Slide 20: Testing
Unit testing: need to figure out how to do this
User Testing: Trial period for candidates to use it for two weeks
- user manual (after GUI is complete)
- developers manual (ongoing)
- Receive feedback from candidates
- Use feedback for improvising the program in the future

## Slide 21: Questions?